## Slide 1: Wireless Communication seminar 3
Sungweon Hong
Information and Intelligent systems lab
Hanyang university
Department of Electronic Engineering

## Slide 2: Contents
Review
  Coherence Bandwidth, Coherence Time
  Discrete time Baseband models
Channel Capacity
  AWGN channel
  Frequency-Flat/Slow-Fading Channel
  Frequency-Flat/Fast-Fading Channel
  Frequency-Selective/Slow-Fading Channel
  Frequency-Selective/Fast-Fading Channel

## Slide 3: Review
Coherence Bandwidth and Power delay profile
Coherence Time and Doppler spread
And they all come from : the time-varying channel impulse response

## Slide 4: Review
The Relationships of the Characteristics
Autocorrelation function
Scattering function
Power Delay Profile
Coherence Bandwidth
Coherence time
Doppler Power Spectrum
Delay Spread
Doppler Spread

## Slide 5: Review
Slow fading Frequency-flat fading | Slow fading Frequency-selective fading
Fast fading Frequency-flat fading | Fast fading Frequency-selective fading
Coherence BW becomes a smaller than signal BW
Coherence
Time
becomes
a smaller
than
symbol duration
“multipath”
“mobility”

## Slide 6: Review
  Frequency Flat / Slow Fading Channel (at time domain)
  Frequency Flat / Fast Fading Channel (at time domain)
  Frequency Selective / Slow Fading Channel
  Frequency Selective / Fast Fading Channel
Channel tracking via Wiener/Kalman filters
OFDM modulation
V2V Communications
Notes: Breaking down widebands into frequency selective channel into several flat channels

## Slide 7
Channel Capacity

## Slide 8: Channel Capacity
What is Channel Capacity?
  The maximum data rates that can be transmitted over the wireless channel with asymptotically small error probability
  https://www.dictionary.com/browse/asymptotic
Scope of this weeks Seminar:
  Capacity of a single-user wireless channel where the transmitter and receiver has a single antenna
    Time-Invariant AWGN channel
    A Flat-Fading Channel
    A Frequency Selective Fading channel

## Slide 9: AWGN Channel
Additive White Gaussian Noise Channel
  SNR (signal-to-noise Ratio) : The ratio of Signal Power to Noise Power
Tx
Rx
(complex value)
power constraint:
Received signal:
Shannon Channel Capacity
[bits/s/Hz]
Shannon Channel Capacity

## Slide 10: AWGN Channel Capacity
What does it mean?
  Channel Capacity is the upper bound of Data Rate that can be sent with negligible errors
  In other words, if the transmission data rate is higher than the Channel Capacity, the receiver cannot recover the message
  We can think Channel as a Cup that can carry water

## Slide 11: AWGN Channel Capacity
Power Constraint signal over bandwidth [Hz]
  SNR (signal-to-noise Ratio) :
Tx
Rx
(complex value)
power constraint:
Received signal:
SNR (signal-to-noise Ratio) :
AWGN Channel Capacity
[bits/s/Hz]
AWGN Channel Capacity

## Slide 12: AWGN Channel Capacity
The performance of a communication system depends on the basic channel resources (e.g., power and bandwidth) available in the channel
  At lower SNR regime, capacity increases linearly with SNR
  At higher SNR regime, capacity increases logarithmically with SNR
AWGN Channel Capacity
[bits/s/Hz]
AWGN Channel Capacity

## Slide 13: AWGN Channel Capacity
The performance of a communication system depends on the basic channel resources (e.g., power and bandwidth) available in the channel
  Fixed power as (figure in next slide) and Increase Bandwidth:
  As
  [bits/s]
AWGN Channel Capacity
[bits/s/Hz]
AWGN Channel Capacity

## Slide 14: AWGN Channel Capacity
Bandwidth limited region
Power limited region
For a fixed power:

## Slide 15
case I:
Frequency-Flat/Slow Fading channel

## Slide 16: Frequency-Flat/Slow Fading Channel
The simplest case and it is nearly a Gaussian channel
  is known only at the receiver
  Thus, the SNR of the channel is
Tx
Rx
Power constraint
Channel Capacity
[bits/s]
Channel Capacity

## Slide 17
case II:
Frequency-Flat/Fast Fading channel